## Slide 1: IMP-EGH: Interdisciplinary Master Program – Energy & Green Hydrogen Track 6: Systems Analysis for Green Hydrogen
3rd Semester | Heidi U. Heinrichs, David Franzmann, Shuying Chen
s.chen@fz-juelich.de
Exercise Unit 5
March 2025

## Slide 2: Renewable energy simulation Schedule
time | agenda
09:00 – 10:15 | Theory portion 1
10:15 – 10:45 | Break
10:45 – 12:00 | Theory portion 2
12:00 – 13:00 | Lunch break
13:00 – 15:00 | Code exercise, questions
Exercise resources download
Class examples: https://github.com/chrisjwin/IMP_EGH_ICE2
Further exploration in ECOWAS area: folder weather_data at https://fz-juelich.sciebo.de/s/BgKPud3OyVZggyV

## Slide 3: Renewable energy simulation Topics
Motivation General Workflow
Overview of weather data
Technologies: solar photovoltaics (PV) energy, Onshore wind energy
  Physical principles
  Workflow
Exemplary Results / H2 Africa application
Python session

## Slide 4: I/O of Renewables Simulation
Output to Energy System Model
Input from LEA
Chart: Placement No. [1]
No | Lon [°] | Lat[°] | Area [m²]
0 | 39.153 | -4.110 | 2814.98
1 | 39.288 | -4.066 | 2739.98
2 | 39.280 | -3.980 | 2444.98
3 | 39.345 | -4.056 | 2274.98
4 | 39.312 | -4.082 | 1979.98
5 | 39.336 | -4.084 | 944.99
… | 39.252 | -4.102 | 1654.98
n | 39.292 | -4.102 | 1794.98
Simulation

## Slide 5: I/O of Renewables Simulation: Geographical Representation
[ref] Winkler, C. et al. Participatory mapping of local green hydrogen cost-potentials in Sub-Saharan Africa. International Journal of Hydrogen Energy 112, 289-321 (2025). https://doi.org:https://doi.org/10.1016/j.ijhydene.2025.02.015
Eligible land
Energy Potential
Renewable Simulation

## Slide 6: RES Potentials: Requirements for Energy System
Resolution:
  High spatial resolution
  Hourly temporal resolution
Variables:
  Capacity of each plant
  Capacity factor time series of each plant
  Cost parameters of each plant

## Slide 7: Overview: General Workflow
Placements
at position x/y
Load all weather data
Process weather data
Simulate renewable energies

## Slide 8: Overview: General Workflow
Placements
at position x/y
Load all weather data
Process weather data
Simulate renewable energies

## Slide 9: Weather Data
[picture] https://www.cen.uni-hamburg.de/icdc/data/atmosphere/reanalysis-atmosphere/ecmwf-era5.html
Usually, we want to simulate future energy systems, but we cannot forecast weather until 2050 (2100)
Use historic weather data and apply statistics
Historic weather data:
Measure data from ground stations
Measure data from satelites / weather balloons
Weather models
Weather data set
Global 2 m Temperature from ECMWF's ERA5 at 1st January 1979 0:00h. Copyright: UHH/CEN/AJB

## Slide 10: Different weather data
[1] https://cds.climate.copernicus.eu/cdsapp#!/dataset/reanalysis-era5-single-levels?tab=overview
[2] https://gmao.gsfc.nasa.gov/reanalysis/MERRA-2/docs/ [3] https://navigator.eumetsat.int/product/EO:EUM:DAT:0863
Dataset | Spatial resolution | Temporal resolution | Scope
ERA 5 | 0.25° x 0.25°, 1940 to present (-5 days) | 1h | Globally
MERRA 2 | 0.5° lat x 0.625° lon, | 1h | Globally
SAHRA 2 | 0.05°x0.05° | 30 min | Europe, Africa
Global Wind Atlas | 300mx300m | Only averages | Globally
Global Solar Atlas | 250mx250m | Only averages | Globally

## Slide 11: ERA 5variables used
Varaible | Technology | Reason
Surface wind speed | PV | Temperature modelling
Surface pressure | PV | Temperature modelling
Surface air temp. | PV | Temperature modelling
Surface dew temperature | PV | Temperature modelling
Global horizontal irradiance | PV | Irradiance modelling
Direct horizontal irradiance | PV | Irradiance modelling

## Slide 12: ERA 5variables used
Varaible | Technology | Reason
Elevated wind speed | Wind | Windspeed model
Surface pressure | Wind | Simulation
Surface air temp. | Wind | Simulation
Boundary layer height | Wind | Windspeed model

## Slide 13: PV

## Slide 14: Overview: General Workflow
Placements
at position x/y
Load all weather data
Process weather data
Simulate renewable energies
Get irradiances at time step and location
Get irradiances on module

## Slide 15: Background 1: Solar Irradiance
[1] Thesis Ryberg

## Slide 16: Background 2: Irradiances Types
GHI: Global horizontal irradiance, DNI: Direct normal irradiance [1] https://www.solaranywhere.com/support/data-fields/definitions/ [2] https://www.researchgate.net/publication/335238562_Availability_Performance_and_Reliability_Evaluation_for_PV_Distributed_Generation/figures?lo=1&utm_source=google&utm_medium=organic
Global horizontal irradiance:
„total irradiance on a horizontal surface plane“
GHI = DHI + DNI∗cos⁡(αzenith​)

## Slide 17: Irradiances Types with ERA5
GHI: Global horizontal irradiance, DNI: Direct normal irradiance DHI: Diffuse horizontal irradiance [1] https://www.solaranywhere.com/support/data-fields/definitions
Available:
  Global horizontal irradiance (good!)
  Direct horizontal irradiance (not good!)
Needed:
  GHI (Global horizontal irradiance)
  DNI (Direct normal irradiance)
    DNI = Direct horizontal irradiance * 1/cos⁡(αzenith​)
  DHI (Diffuse horizontal irradiance)
    DHI = GHI – DNI ∗ cos⁡(αzenith​)
αzenith needed: solar position and time series need to be matched

## Slide 18: Long Run Averages (LRA)
GHI: Global horizontal irradiance, DNI: Direct normal irradiance
ERA5: hourly resolution, but only 0,25° (20km at lat45°) resolution
Global solar atlas: resolution of 250m, but only 40-year average
Can this be combined?
High res
Low res
High res + hourly
hourly

## Slide 19: Overview: General Workflow
Placements
at position x/y
Load all weather data
Process weather data
Simulate renewable energies
Get irradiances at time step and location
Get irradiances on module

## Slide 20: Plane of Array (POA)
irradiance data is transposed to the plane of the array
: Energy which hits the actual array
  direct beam
  : ground reflected
  : diffuse radiation
Depending on:
  sun position
  Array orientation and tracking
  Irradiance components (DNI, DHI)
  Ground albedo
[1] https://pvpmc.sandia.gov/modeling-guide/1-weather-design-inputs/plane-of-array-poa-irradiance/

## Slide 21: Overview: General Workflow
Placements
at position x/y
Load all weather data
Process weather data
Simulate renewable energies
Get irradiances at time step and location
Get irradiances on module

## Slide 22: Simulation Step 1: Estimation of Cell Temperature
[1] https://pvlib-python.readthedocs.io/en/stable/reference/generated/pvlib.temperature.sapm_cell.html?highlight=pvlib.temperature.sapm_cell
Temperature can be estimated from empirical model:
Based on:
  Irradiance on module: POA
  Ambient temperature:
  Empirical model of windspeed and calibration parameter:
Based on PV-Lib (parameters and equations) [1]

## Slide 23: Simulation Step 2: Calculation of Power Output
[1] W. De Soto et al., “Improvement and validation of a model for photovoltaic array performance”, Solar Energy, vol 80, pp. 78-88, 2006. [2] https://pvlib-python.readthedocs.io [fig] https://www.atonometrics.com/applications/what-is-a-pv-module-iv-curve/
Calculation of the single diode equation from De Soto et al. [1]
Solve the single diode equation to obtain a photovoltaic IV curve [2]
Irradiance, temperature and electrical module params from PVlib database [2]

## Slide 24: Result: PV Potentials
Apply this algrithm for each placement (up to millions) and different weather years to calculate average potential

## Slide 25: Wind

## Slide 26: Background
[fig left] https://doi.org/10.3390/en12071208 [fig right] Thesis Ryberg
Energy from wind:
Maximal technical extractable power: (Betz law, not an efficiency)
Windspeed is intermittent. Therefore, distributions are often modelled as Weibull distributions
Wind creates a boundary layer above the surface

## Slide 27: Overview: General Workflow
Placements
at position x/y
Load all weather data
Process weather data
Simulate renewable energies
Get wind speed at time step and location
Model wind speed at turbine height

## Slide 28: Long Run Averages (LRA)
GHI: Global horizontal irradiance, DNI: Direct normal irradiance
ERA5: hourly resolution, but only 0,25° (20km at lat45°) resolution
Global wind atlas: resolution of 250m, but only 40-year average
Can this be combined?
High res
Low res
High res + hourly
hourly

## Slide 29: Overview: General Workflow
Placements
at position x/y
Load all weather data
Process weather data
Simulate renewable energies
Get wind speed at time step and location
Model wind speed at turbine height

## Slide 30: Projection to Wind Speed

## Slide 31: Overview: General Workflow
Placements
at position x/y
Load all weather data
Process weather data
Simulate renewable energies
Get wind speed at time step and location
Model wind speed at turbine height

## Slide 32: Power Curve
Power curve: electrical power determined by the wind speed
Real generation is distrubuted around the ideal generation due to:
  Dynamic effects
  Wind shears
  Wind speed estimations
  Changing air density …

## Slide 33: Power Curve
Convolution used as statistical measure to account for these effects

## Slide 34: Result: Onshore Wind Potentials
Apply this algorithm for each placement (up to millions) and different weather years to calculate average potential

## Slide 35: Cost model

## Slide 36: Determining the LCOE
Levelized costs of electricity (LCOE): the average net present cost of electricity generation for a generator over its lifetime
Costs:
  Investment costs (2050: , ~)
  Operation and maintenance costs (2% Invest/a)
  Fuel costs (usually zero)
  Carbon dioxide mitigation costs (usually zero)
Energy:
  electrical energy per year (from simulation)
Other:
  Discount rate (here 8%)
  n: lifetime (20-25 years)
Notes: Discount rate accounts for the time value of money - the idea that money today is worth more than the same amount in the future. (to consider inflation in the project costs calculation)
The higher discount rate, the higher LCOE and make the project less attractive (the future revenue is worth less).

## Slide 37: Cost assumptions
[1] Stolten et al.; KSG2045; 2023
Notes: Operation and Maintenance (O&M) Costs, shown as percentage of Capital Expenditure (CAPEX)

## Slide 38: Cost Potential of Renewable Energies
H2Atlas project: https://africa.h2atlas.de/africa

## Slide 39: Python Implementation:
IEK-3 developed Python-tool. ETHOS.RESkit

## Slide 40: ETHOS: Energy Transformation PatHway Optimization Suite
Renewable Energy
Resources
Buildings
Electricity transmission & distribution grids
Gas transmission grid
H2 global
H2 and PtX
Infrastructure
Districts
From demand to load profile
Cost optimized energy systems
Regionalized via local demand and
infrastructure
Integrated Hourly Optimization
Single-node
< 400 nodes
Technology Database
Societal feasibility
Transport sector
Passenger
Freight
Activity-based transport demand
Life Cycle Assessment*
Macro-economics*

## Slide 41: Python Implementation:
IEK-3 developed Python-tool. ETHOS.RESkit
Publicly available at:
  https://github.com/FZJ-IEK3-VSA/RESKit/tree/master

## Slide 42: Simulation of PV: Placements as Input Data

## Slide 43: PV Simulation
Output: Placements with results
Input: Placements from results
Input: Path to ERA-5 data
Input: Path to GSA (GHI/DNI)

## Slide 44: Whole Code for PV:

## Slide 45: Simulation of PV: Results are Different Variables as Time Series

## Slide 46: Simulation of Wind: Placements as Input Data

## Slide 47: Wind Simulation
Output: Placements with results
Input: Placements from results
Input: Path to ERA-5 data
Input: path to global wind atlas
Input: path to land cover dataset

## Slide 48: Simulation of Wind: Results are Different Variables as Time Series